## Slide 1
Aggressive Maneuver Planning and Control of a Multi-UAV and Payload System after a Failure
Master Thesis Defense
Presented by: Alvin Isac PREMSUNDER
14 October 2025
Supervisors: Prof. Marco Baglietto, Prof. Olivier Kermorgant, Dr. Andrea Delbene
UNIVERSITÉ DE GENOVA | ÉCOLE CENTRALE DE NANTES | GRAAL
Notes: “Good morning everyone, and thank you for being here. My name is Alvin Isac Premsunder, and today I’ll be presenting my Master’s thesis defense titled ‘Aggressive Maneuver Planning and Control of a Multi-UAV and Payload System after a Failure.’ This work was carried out as part of a joint program between the University of Genova and École Centrale de Nantes, in collaboration with the GRAAL research group. I was guided by my supervisors — Professor Marco Baglietto, Professor Olivier Kermorgant, and Dr. Andrea Delbene. I’ll begin by giving you an overview of the motivation behind the work, the problem we addressed, the control approach we developed, and the key results we obtained.”

## Slide 2
Introduction & Motivation
UAVs (Unmanned Aerial Vehicles) are widely used in agriculture, delivery, surveillance, inspection, and rescue missions.
Recent advances in autonomous control have enabled complex multi-UAV operations.
Cooperative UAVs can share tasks, transport heavier payloads, and improve safety and efficiency.
Photo credits: James Gibson, DRONE EFT & Will Porada on Unsplash
2 / 21
Notes: “Before going into the problem we worked on, I’ll start with a brief introduction about UAVs and why they are important today. in earlier years UAVs were developed mainly for military and surveillance purposes, but over the years they have evolved and become widely used in civilian applications such as agriculture, inspection, delivery, and search and rescue.” With the progress in control systems, we can now make multiple UAVs work together for tasks like cooperative payload transport. This kind of operation helps carry heavier loads, improves efficiency, and allows work in areas where human access is difficult.

## Slide 3
When one UAV in a cooperative transport system fails, the sudden load redistribution creates an immediate and dangerous swinging motion of the payload. Without a specialized control
strategy, these oscillations can escalate, leading to mission failure or collisions.
3 / 32
Problem Statement & Motivation
How to rapidly suppress severe payload oscillations after a UAV failure?
How to maintain coordinated and stable flight among the remaining UAVs?
How to ensure the system can transition back to safe and continue the mission after stabilization?

## Slide 4
Objectives & Research Contributions
Objectives of the thesis
Proposed a two-phase control framework for post-failure stabilization and tracking with remaining UAV and payload system.
Introduced a fault-tolerant optimization strategy that enables aggressive stabilization for quick recovery.
Demonstrated through simulations that the approach achieves rapid oscillation damping and trajectory tracking after stabilization.
4 / 32
Main Contribution
• Develop and test algorithms that allow the remaining UAVs to:
• Reconfigure their formation to maintain control of the payload.
• Dampen oscillations rapidly and restore stability through aggressive maneuvers.
• Implement and validate these strategies in simulation like (ROS2/Gazebo and MATLAB)

## Slide 5
State of the Art
Multi UAVs payload system
Single-UAV cable-suspended payload system
Elastic cable model for UAV payload system
Xian, B., Wang, S. & Yang, S. (2019). Nonlinear adaptive control for an unmanned aerial payload transportation system: theory and experimental validation. Nonlinear Dynamics, 98, 1745–1760
Kotaru, P., Wu, G. & Sreenath, K. (2017). Dynamics and control of a quadrotor with a payload suspended through an elastic cable. In 2017 American Control Conference (ACC), 3906–3913, IEEE.
Alothman, Y.N. (2018). Optimal control of multiple quadrotors for transporting a cable suspended payload.
5 / 32

## Slide 6
State of the Art
Delbene, A. & Baglietto, M. (2024). Recovery techniques for a multi-uav system transporting a payload. In 2024 IEEE 20th International Conference on Automation Science and Engineering (CASE), 559–566, IEEE.
Delbene, A. & Baglietto, M. (2024). Cables tension modeling for multi-uav payload transportation. In 2024 IEEE 20th International Conference on Automation Science and Engineering (CASE), 212–218, IEEE.
6 / 32

## Slide 7
State of the Art
Delbene, A. & Baglietto, M. (2024). Recovery techniques for a multi-uav system transporting a payload. In 2024 IEEE 20th International Conference on Automation Science and Engineering (CASE), 559–566, IEEE.
Delbene, A. & Baglietto, M. (2024). Cables tension modeling for multi-uav payload transportation. In 2024 IEEE 20th International Conference on Automation Science and Engineering (CASE), 212–218, IEEE.
7 / 32
Architectural Similarities to Present Thesis:
Key Differences:
➤ Spring-damper cable modeling approach
➤ Fault-tolerant controller
➤ Recovery methodology
➤ Dynamic formulation
• Anchor points: Off-COM vs. COM-based present thesis.
• Control method: PID + ISMC + CB vs. NMPC optimization
• Recovery strategy: Rule-based vs. Aggressive Stabilization

## Slide 8
Simulation Setup
Dual-platform setup for prototyping and controller validation
MATLAB/Simulink
ROS2/Gazebo
PX4 autopilot integration
ROS2 <--> PX4 communication via XRCE-DDS
QGroundControl monitoring & telemetry
High-fidelity physics simulation in Gazebo
8 / 32
Rapid NMPC tuning & prototyping
Realistic discrete–continuous system modeling
Fast cost & constraint iteration
Parameter sensitivity analysis
Stability and convergence testing
Transition testing before ROS2 integration

## Slide 9
Core Idea behind the Control Approch
9 / 32
Top view
Front view
Side view

## Slide 10
Core Idea behind the Control Approch
9 / 32
Top view
Front view
Side view

## Slide 11
Controller Selection: NMPC
Nonlinear Model Predictive Control (NMPC) is an advanced control strategy that most Extensively Researched Control Framework for UAV Systems which is uniquely suited for this problem.
Why NMPC why not other controllers?
Predictive Nature
Constraint Handling
Robust performance
Multi-Objective Optimization
Natively handles the complex dynamics
MPC Control Structure
NMPC Formulation
Chen, J., Tian, G. & Fu, Y. (2023). A novel multi-objective tuning strategy for model predictive control in trajectory tracking.
Journal of MechanicalScience and Technology, 37, 6657–6667.
10 / 32

## Slide 12
Disadvantages of the NMPC?
MPC Control Structure
NMPC Formulation
Chen, J., Tian, G. & Fu, Y. (2023). A novel multi-objective tuning strategy for model predictive control in trajectory tracking.
Journal of MechanicalScience and Technology, 37, 6657–6667.
11 / 32

## Slide 13
Disadvantages of the NMPC?
MPC Control Structure
NMPC Formulation
Chen, J., Tian, G. & Fu, Y. (2023). A novel multi-objective tuning strategy for model predictive control in trajectory tracking.
Journal of MechanicalScience and Technology, 37, 6657–6667.
12 / 32
1. Model Sensitivity

## Slide 14
Mathematical Model
The effectiveness of the NMPC controller heavily relies on an accurate mathematical model.
Urbina-Brito, N., Guerrero-Sánchez, M.E., Valencia-Palomo, G., Hernández-González, O., López-Estrada, F.R., & Hoyo-Montaño, J.A. (2021). A predictive control strategy for aerial payload transport using an unmanned aerial vehicle. Mathematics, 9, 1822.
13 / 32
Quadrotor with a cable-suspended payload

## Slide 15
Mathematical Model
The effectiveness of the NMPC controller heavily relies on an accurate mathematical model.
Liang, X., Zhang, Z., Yu, H., Wang, Y., Fang, Y. & Han, J. (2022). Antiswing control for aerial transportation of the suspended cargo by dual quadrotor uavs. IEEE/ASME Transactions on Mechatronics, 27, 5159–5172.
Multi-UAV cooperative payload transport system
14 / 32

## Slide 16
Mathematical Model
The effectiveness of the NMPC controller heavily relies on an accurate mathematical model.
Alothman, Y. & Gu, D. (2018). Using constrained nmpc to control a cable-suspended payload with two quadrotors. In 2018 24th International Conference on Automation and Computing, 1–6, IEEE.
Alothman, Y.N. (2018). Optimal control of multiple quadrotors for transporting a cable suspended payload.
15 / 32

## Slide 17
Mathematical Model
The effectiveness of the NMPC controller heavily relies on an accurate mathematical model.
Alothman, Y. & Gu, D. (2018). Using constrained nmpc to control a cable-suspended payload with two quadrotors. In 2018 24th International Conference on Automation and Computing, 1–6, IEEE.
Alothman, Y.N. (2018). Optimal control of multiple quadrotors for transporting a cable suspended payload.
15 / 32

## Slide 18
Mathematical Model
The effectiveness of the NMPC controller heavily relies on an accurate mathematical model.
Delbene, A. & Baglietto, M. (2024). Recovery techniques for a multi-uav system transporting a payload. In 2024 IEEE 20th International Conference on Automation Science and Engineering (CASE), 559–566, IEEE.
16 / 32
Cable Tension Modeling
Quadrotor Dynamics
Quadrotor Translational Dynamics:
Quadrotor Rotational Dynamics:
Payload Dynamics
Payload Translational Dynamics:

## Slide 19
Disadvantages of the NMPC?
MPC Control Structure
NMPC Formulation
Chen, J., Tian, G. & Fu, Y. (2023). A novel multi-objective tuning strategy for model predictive control in trajectory tracking.
Journal of MechanicalScience and Technology, 37, 6657–6667.
17 / 32
MODEL SENSITIVITY
COMPUTATIONAL RESOURCES

## Slide 20
NMPC Implementation Setup
Workineh, Y., Mekonnen, H., & Belete, B. (2024). Numerical methods for solving second-order initial value problems of ordinary differential equations using Euler and fourth-order Runge–Kutta methods. Frontiers in Applied Mathematics and Statistics, 10.
Andersson, J.A.E., Gillis, J., Horn, G., Rawlings, J.B., & Diehl, M. (2018). CasADi: a software framework for nonlinear optimization and optimal control. Mathematical Programming Computation
18 / 32
Optimization Framework
Several toolchains are used in real-time NMPC reseach: CasAdi, ACADO, Forces Pro, FiMCON etc.
Discretization Method
We selected CasADi because it provides:
  Easy Prototyping
  Large and active community support
  Programming interface Python / MATLAB / C++
  Enables real-time NMPC computation
Trade-off: RK4 provides higher accuracy but 4 times higher computational cost. While Euler is faster, easier to implement, and provides sufficient accuracy.

## Slide 21
NMPC Configuration & Parameters
19 / 32
Parameter values were optimized through iterative simulation and experimental validation.
Prediction Horizon
Control Horizon (Nc)
Sampling / Discretization Time (Δt)
Constraint violation tolerance
Maximum solver iterations
Maximum step tolerance
Input constraint tolerance
Control Input Constraints
State Constraints
Warm Starter Formulation

## Slide 22
Phase 1: Aggressive Stabilization
20 / 32
Terminal cost:

## Slide 23
Phase 2: Precision Tracking
21 / 32
Terminal cost:

## Slide 24
The Two-Phase NMPC Strategy
22 / 32
Phase 1: Aggressive Stabilization
Phase 2: Precision Tracking
A single controller is not optimal for both emergency recovery and normal flight. We developed a two-phase strategy that switches the NMPC’s objective (cost function) based on the system’s stability.
Phase Switching Logic
The controller transitions from Phase 1 to Phase 2 when the payload and UAV velocities fall below a predefined threshold (e.g., < 0.05 m/s), indicating the system is stable.

## Slide 25
Results: Scenario 1 – Tracking without Stabilization
23 / 32
Altitude

## Slide 26
Results: Scenario 2 – Stabilization then Tracking
24 / 32
Altitude

## Slide 27
Conclusion
25 / 32
We successfully developed and validated a two-phase NMPC framework for fault-tolerant control of a multi-UAV payload system.
The dedicated aggressive stabilization phase is proven to be critical for safety, rapidly suppressing dangerous post-failure oscillations.
The framework demonstrates a seamless transition to a precision tracking phase, allowing the mission to continue after recovery.
Unfortunately, due to a communication error/bug between ROS2 and PX4, we were not able to fully test the controller performance in the Gazebo simulation. However, this limitation was related to the ROS interface, not the proposed NMPC algorithm itself.

## Slide 28
Future Work
26 / 32
Finalize ROS2/Gazebo Integration
Enhanced Simulation Testing
Advanced NMPC Methodologies
Laboratory Experimental
Onboard Implementation

## Slide 29
Selected References
A. Delbene and M. Baglietto, “Cables tension modeling for multi-UAV payload transportation,” Proc. 2024 IEEE 20th Int. Conf. on Automation Science and Engineering (CASE), pp. 212–218, IEEE, 2024.
2. A. Delbene and M. Baglietto, “Recovery techniques for a multi-UAV system transporting a payload,” Proc. 2024 IEEE 20th Int. Conf. on Automation Science and Engineering (CASE), pp. 559–566, IEEE, 2024.
3. Y. Alothman and D. Gu, “Using constrained model predictive control to control two quadrotors transporting a cable-suspended payload,” Proc. 2018 13th World Congress on Intelligent Control and Automation (WCICA), pp. 228–233, IEEE, 2018.
4. P. Kotaru, G. Wu, and K. Sreenath, “Dynamics and control of a quadrotor with a payload suspended through an elastic cable,” Proc. 2017 American Control Conference (ACC), pp. 3906–3913, IEEE, 2017.
5. G. Li and G. Loianno, “Nonlinear model predictive control for cooperative transportation and manipulation of cable-suspended payloads with multiple quadrotors,” Proc. 2023 IEEE/RSJ Int. Conf. on Intelligent Robots and Systems (IROS), pp. 5034–5041, IEEE, 2023.
27 / 32

## Slide 30
Acknowledgements
28 / 32
I would like to express my sincere gratitude to my supervisors, Prof. Marco Baglietto, Prof. Olivier Kermorgant, and Dr. Andrea Delbene, for their invaluable guidance and support throughout this thesis.
I would like to extend thanks to Prof. Carmine Recchiuto for providing the computing resources essential to completing this thesis.
My thanks also go to the EMARO team at École Centrale de Nantes, the University of Genova, and the GRAAL laboratory for providing the environment and resources that made this research possible.
Special thanks to my family for their unconditional love and encouragement.

## Slide 31
Thank You !!
Thank you for attending this thesis defense.
Your presence and engagement are greatly appreciated.
Presented by: ALVIN ISAC PREMSUNDER
Student ID: s7789223
Email: alvinisac3399@gmail.com |
alvin-isac.prem-sunder@eleves.ec-nantes.fr
Questions are welcome